## Slide 1: Hardware Workshop One Fundamentals
Day 1 Start

## Slide 2: Motivation
Have no spring/summer activities in ECE
Review some concepts learned in ECE110
Learn some new concepts for ECE212 & ECE231
Have some ideas about how to build and debug a circuit
Build something practical out of simple components
Get motivated to design/build on your own and have fun

## Slide 3
Iris Wang - ECE 2T5
irisjiayi.wang@mail.utoronto.ca
Staff
Shuntaro Wakamatsu - ECE 2T5
shuntaro.wakamatsu@mail.utoronto.ca
Nicholas Mutlak - ECE 2T5
n.mutlak@mail.utoronto.ca
Ryan Seto - ECE 2T5
ryan.seto@mail.utoronto.ca
Simon Xu - ECE 2T5
xiaofengsimon.xu@mail.utoronto.ca

## Slide 4: Hardware Workshop: (4 Day Program)
Phase One: Review of Ece110
  Resistor, Capacitor, Inductor
  Series and Parallel Circuits
  Breadboard
  Soldering
  Digital Multimeter
  Function Generator
  Oscilloscope

## Slide 5: Hardware Workshop: (4 Day Program)
Phase Two: Introduction to Ece212/231
  Semiconductor
  Diode and LED
  Types of Transistors
  NPN and PNP Connections
  Astable Multivibrator
  Operational Amplifiers

## Slide 6: Hardware Workshop: (4 Day Program)
Phase Three: Application Part 1
  DC Motors
  Pulse Width Modulation
  H-Bridge
  Photoresistors
  Phototransistors
  Colour Detection

## Slide 7: Hardware Workshop: (4 Day Program)
Phase Four: Application Part 2
  Coupled Inductors
  Joule Thief
  Generators
  Workshop Competition

## Slide 8: Resistor, Capacitor & Inductor
Review

## Slide 9: Free Electron
Current is the flow of charge
Free electrons carry charge
Number of free electrons determines conductivity of a material
Current (I, i) is charge in motion
Conventional current is in the opposite direction of electrical current

## Slide 10: Resistor
Opposes flow of current
Usage:
  Limits current
  Turns current into voltage
  Works as a Voltage Divider

## Slide 11: Capacitor
  Stores energy in an electric field
  Opposes sudden changes in voltage
  Z =

## Slide 12: Inductor
  Stores energy in a magnetic field
  Opposes sudden changes in current
  Z =

## Slide 13: Series and Parallel Connections

## Slide 14: Digital Multi-Meter (DMM) & Breadboard
Review

## Slide 15: DMM
Using the DMM as a Voltmeter
Plug Red Probe into V/Ω
Select AC/DC based on type of measurements
Connect the Voltmeter in parallel with the circuit
The DMM will measure the voltage across its probes

## Slide 16: DMM
Using the DMM as an Ohmmeter
Plug Red Probe into V/Ω
Connect the Ohmmeter in parallel with the circuit with no source
The DMM will measure the resistance between its probes

## Slide 17: DMM
Using the DMM as an Ammeter
Plug the Red Probe into A
Select AC/DC based on type of measurements
Connect the ammeter in series with the circuit
The DMM will act as a short and measure the current through its probes

## Slide 18
Use the continuity test on the digital multi-meter to find out how the breadboard is connected
A1: Breadboard Connections

## Slide 19: A1: Breadboard Connections

## Slide 20: A1: Breadboard Connections

## Slide 21: A1: Breadboard Connections

## Slide 22: New
Soldering

## Slide 23: Soldering
The process of joining different types of metal by melting solder and using it as a kind of glue
You’ll need a soldering iron, soldering station, and helping stand

## Slide 24: Soldering Iron
Used to melt the solder and heat the two wires you are connecting

## Slide 25: Soldering Station: Safety
Safety standards when using a soldering iron
  Always assume the iron is hot
  Put the iron back to the station’s iron holder after use
  Make sure any components being soldered together are disconnected from any power source

## Slide 26: Soldering Station: Clean tip
Clean the tip before use
  Use iron holder’s wet sponge or brass sponge to remove the oxidation on the soldering iron tip
  Oxidation does not allow heat to transfer, hence, resulting in a poor connection dubbed “cold solder”

## Slide 27: Soldering: The Process

## Slide 28: A2: Soldering Practice
Solder at least 4 resistors together to make the first letter of your name
As a requirement of your design, ensure you use at least 2 resistors of the same value directly in series with each other
Calculate equivalent resistance of your circuit
Verify your calculation with DMM

## Slide 29
Review
Oscilloscope & Function Generator

## Slide 30: Function Generator

## Slide 31: Function Generator
Power button
Signal shape selection
Frequency multiplier switch
Frequency dial
EXT/INT selector
Frequency display
Duty Control
Amplitude control
DC Offset control
Output BNC connector

## Slide 32
There are many models with the same basic functionalities but may offer different features
Oscilloscope: Models

## Slide 33: Oscilloscope: Usage
Determining the frequency, amplitude, phase of a signal, which is critical when debugging a circuit
Identifying how much noise is in the circuit
Identifying the shape of a wave -- sine, square, triangle, sawtooth, complex, etc.
Quantifying phase differences between two different signals

## Slide 34: Oscilloscope: Probes
Have the same common ground for all the probes
Be aware of the probe scaling (multiplication factor)
Attach the tip to the signal to be measured
Attach ground clip to a known ground

## Slide 35: Oscilloscope: Adjusting
Adjusting position and scale of the signal
Vertical Control:
Set value per grid division to display
horizontal Control:
How many seconds per grid division are displayed

## Slide 36: Oscilloscope: Built-in Function Generator
Create a signal
Select source
Select parameter with intensity knob
Turn output on
Metal BNC connectors labeled source 1 & 2
  Outputs of the integrated signal generator

## Slide 37
Things to keep in mind:
  Check if the multiplication factor on the probe matches the setting on oscilloscope
  Properly connect the ground of the probe
  Adjust to proper scale to see the signal
    If in doubt can use the “Auto” setup as a starting point
Oscilloscope: Final Tips

## Slide 38: A3: Voltage Divider
Use the built-in function generator of the oscilloscope to produce a 2V peak-to-peak 10kHz sine wave and measure it using the oscilloscope
Use the previous circuit you soldered as a voltage divider, with the intention of halving the amplitude of the input signal. Recall its unique design specification. Measure this output signal
Use the oscilloscope’s cursors to verify the frequency and the amplitude
Notes: Can provide a quick demo

## Slide 39: Hardware Workshop One Fundamentals
Day 1 End

## Slide 40: Hardware Workshop One Diodes, Transistors and OpAmps
Day 2 Start

## Slide 41: Diode
New

## Slide 42: Semiconductor
Commonly used semiconductor: silicon and germanium
  Doped into N-type or P-type semiconductor
  Useful for PN junctions
Charge carrier: electrons or holes that contribute to the flow of current
  N-type charge carrier: electron
  P-type charge carrier: hole

## Slide 43: Semiconductor: PN Junction
Depletion region creates boundary inhibiting electron movement when unbiased.
A voltage is required to overcome the boundary inhibiting electron movement (forward bias).

## Slide 44: Diode
Only allow current to pass in one direction
Basically a PN junction
Forward voltage required to overcome depletion region (typically 0.7V)

## Slide 45: LED (Light Emitting Diode)
Act like a diode but emit light when on
Require higher voltage to turn on (2.8 – 3.6V)
Made of gallium arsenide and gallium phosphide whose electrons emit light when transferring energy

## Slide 46: A4: Testing Diodes by DMM

## Slide 47
Try to use one diode to turn AC into only one polarity.
Measure the waveform of the output using oscilloscope.
A5: Half-Wave Rectifier

## Slide 48
Challenge now: Can you build a rectifier which turns the other half into the same polarity?
A5: Full-Wave Rectifier

## Slide 49
A5: Full-Wave Rectifier

## Slide 50: Transistor
New

## Slide 51: Transistor
Transistor is a semiconductor device used as a switch or to amplify electronic signals
Transistors are widely used in modern electronics
Types of transistor:
  Bipolar junction transistor (BJT)
  Metal-oxide-silicon field effect transistor (MOSFET)

## Slide 52: Transistor (BJT)
Stack of doped semiconductor materials (NPN or PNP junctions)
Base-Emitter junction controls the flow of current
Can be used as switch or amplifier depends on mode of operation.

## Slide 53
Cut-Off: (Off Switch Region)
  Base-Emitter and Base-Collector junction are both reverse biased
  No current through Collector to Emitter
Saturation: (On Switch Region)
  Base-Emitter and Base-Collector junction are both forward biased
  Low impedance from Collector to Emitter
Active: (Amplifier Region)
  Base-emitter forward biased and Base-collector reverse biased
  Amplification of current controlled by Base-Emitter voltage
Transistor - BJT Operation Regions

## Slide 54
A6: Astable Multivibrator
Produces square waves
Uses transistor as the switch to charge and discharge capacitors

## Slide 55: A6: Astable Multivibrator

## Slide 56: A6: Astable Multivibrator

## Slide 57: A6: Astable Multivibrator

## Slide 58: A6: Astable Multivibrator with LED Output (SWAP WITH LIVE DEMO)

## Slide 59
New
Operational Amplifiers

## Slide 60
Operational Amplifier (Op Amp)
Zin → ∞ Ω (open circuit)
Zout → 0 Ω (short circuit)
A → ∞ (very large gain)
Output is capped by the V+/- rails in the top and bottom that power the Op Amp

## Slide 61
Op Amp: Stabilizing Output
Negative feedback
  Make the Op Amp dependent on the feedback of the output
  Gives us some control in influencing the Op Amp’s output through modifying the negative feedback wire
  Use the input current to the +/- nodes = 0, voltages of the +/- nodes are a virtual short (V+ = V-), and KCL analysis to do this

## Slide 62
Op Amp: Configurations

## Slide 63
A7: Building Amplifiers
Try to build an inverting amplifier with Gain bigger than 5. What happens?
Build a summing Op Amp with 2 inputs and Vout = -(V1 + V2)

## Slide 64
Consider the Astable Multivibrator with only a 2.0V source
Enough to charge and switch the transistors but not enough to power the LEDs
Add an amplifier to one side of the circuit to make one LED flash on and off, while the other does not
A8: Amplifying Astable Multivibrator

## Slide 65: Hardware Workshop One Diodes, Transistors and OpAmps
Day 2 End

## Slide 66: Hardware Workshop One Motor Control and Light Sensors
Day 3 Start

## Slide 67: DC Motors

## Slide 68: Modelling DC Motors
Current flows into the motor
Magnetic force is generated to spin the shaft
How can we model this system?
Notes: We will talk more about Faraday’s Law tomorrow

## Slide 69: Modelling DC Motors
What direction will the motor spin?

## Slide 70: Modelling DC Motors: Important Attributes
We need to be able to implement:
1. Variable Speed
2. Variable Direction

## Slide 71: Pulse Width Modulation (PWM)
What happens if I pulse my DC input voltage on and off very, very quickly?
Light gets dimmer, as ON pulses get shorter and OFF pulses get longer
Notes: Reference spikes

## Slide 72: A9: Play with PWM and Motors
Set up a PWM signal (10kHz, 10V) on your function generators and connect it directly to a DC motor
Adjust the Duty Cycle of the PWM signal and observe how the RPM of the motor changes

## Slide 73: H-Bridge

## Slide 74: So Far, Only One Direction
How can we control the direction that the motor spins?
Solution: H-Bridge Circuit
NPN Transistors
Notes: How we can control which way the current flows through the motor
Model switches with transistors

## Slide 75: Modelling DC Motors
What happens if we provide a DC Motor with AC voltage?
The inductor in the motor will store up energy in a magnetic field
When the voltage across it changes rapidly, it will want to discharge that energy, but in reverse polarity to the voltage that was across it
Notes: Problem with changing voltage quickly
Current needs time to change
Results in Voltage Spikes if the current has nowhere to go -> damage transistors

## Slide 76: Flyback Diodes
How do we prevent the motor’s inductance spikes from damaging our transistors?
Solution: Flyback Diodes

## Slide 77: A10: Build a Winch
We can use an H-bridge circuit with
  NPN transistors modelled as our switches
  Resistive loads to mitigate shoot-through situations
  Flyback diodes to manage inductive spikes
Now let’s build it: Build an H-bridge with Vcc: 10V power supply using the function generator and your DC Power Supply to power your switches.
  Recall not to cause a shoot through scenario by powering SW1 and SW2 / SW3 and SW4 at the same time, as this will damage your transistors

## Slide 78: A11: Build a Better Winch
How can we incorporate variable speed with PWM like we learned before into our H-Bridge Circuit?

## Slide 79: Light / Colour Detector

## Slide 80: Variable Resistors: Potentiometers
Allow for resistance to be controlled by some external variable
10K Potentiometer (POT)
  Ranges from 0 – 10kΩ
Pins 1 -> 3 are set 10kΩ
Pins 2 -> 1 or 2 -> 3 is a variable resistance depending on where the wiper is
  More track between pins = More resistance

## Slide 81: Variable Resistors: Photoresistors
Photocells, Light Dependent Resistor (LDR)
Allows for resistance to be controlled by light
  More light = Less resistance
  More dark = Larger resistance

## Slide 82: Photoconductive Effect
Photoconductive Effect: When light shines on a material, electrical conductivity increases
Photons excite electrons -> more energy in material -> more conductivity
Property is prominent in materials like Cadmium Sulfide (CdS Photoresistors)

## Slide 83: A12: Build a Phototransistor to Detect Colour
Use both a potentiometer and photoresistor to tune a transistor to light up an LED only when a specific colour is detected
  Note: Colours absorb other lighter colours and reflect other darker colours

## Slide 84: Hardware Workshop One Motor Control and Light Sensors
Day 3 End

## Slide 85: Hardware Workshop One Generating Power
Day 4 Start

## Slide 86
Coupled Inductors

## Slide 87
Two coils are placed nearby or winded on the same core
  Magnetically coupled
Magnetic core holds the magnetic flux
  The same magnetic flux pass through two coils
  Change of magnetic field in one coil will induce current in the other coil.
Coupled Inductor

## Slide 88
Dot convention:
  With the same direction of magnetic flux, current flows into the dot
Aiding mode:
  Dot at the same side
Opposing mode:
  Dot at opposite side.
Coupled Inductor

## Slide 89
Coupled Inductor

## Slide 90
Wind an aiding mode coupled inductor on a ferrite core and measure the primary & secondary side voltage using oscilloscope
Wind an opposing mode coupled inductor on a ferrite core and measure the primary & secondary side voltage using oscilloscope
A13: Coupled Inductor

## Slide 91
Joule Thief

## Slide 92: A14: Joule Thief
The joule thief is a self-oscillating voltage booster using coupled inductor.
  Convert constant low voltage to a periodical higher voltage.
Typically used to drive small loads

## Slide 93
Generators

## Slide 94: Hand Crank: Mechanical Energy
Works through application of Faraday’s Law
Rotate the wheel with your hand via a crank
Rotation of the magnets relative to the wound-up wire induces a current within wire
Faster rotation = Faster movement through magnetic field = Stronger induced current

## Slide 95: Solar Panels: Solar Energy
Photovoltaic Effect:
  Photons will excite electrons in the depletion zone of PN junction
  Split electrons and holes are pushed to their respective sides
  This creates a small potential difference across the junction
Put enough photovoltaic cells in series or parallel with each other and you can get a substantial voltage
Notes: Recall PN junctions and photoconductive effect

## Slide 96
Day 4 Competition

## Slide 97: Competition Outline (subject to change atm)
Generate the highest possible voltage you can from the tools you have been given to power your flashlight
You may use any of the tools / concepts we have covered
Bonus points if you manage to incorporate the Joule Thief circuit into your design in a practical manner
You cannot use the function generator or oscilloscope to generate any voltage

## Slide 98: Hardware Workshop One Generating Power
Day 4 End